## Slide 1: DATA COMMUNICATION
CSE 225/233
WEEK-11, LESSON-1 & 2
ERROR DETECTION

## Slide 2: Polynomial
A better way to understand cyclic codes and how they can be analyzed is to represent them as polynomials. A pattern of 0s and 1s can be represented as a polynomial with coefficients of 0 and 1. The power of each term shows the position of the bit; the coefficient shows the value of the bit.

## Slide 3: CRC Division using polynomial

## Slide 4: Standard Polynomial

## Slide 5: Checksum
Checksum is an error-detecting technique that can be applied to a message of any length. In the Internet, the checksum technique is mostly used at the network and transport layer rather than the data link layer.
At the source, the message is first divided into m-bit units. The generator then creates an extra m-bit unit called the checksum, which is sent with the message. At the destination, the checker creates a new checksum from the combination of the message and sent checksum. If the new checksum is all 0s, the message is accepted; otherwise, the message is discarded.
Conceptual figure of checksum in presented in the next slide.

## Slide 6: Checksum (Concept)

## Slide 7: Example
Suppose our data is a list of five 4-bit numbers that we want to send to a destination. In addition to sending these numbers, we send the sum of the numbers. For example, if the set of numbers is (7, 11, 12, 0, 6), we send (7, 11, 12, 0, 6, 36), where 36 is the sum of the original numbers. The receiver adds the five numbers and compares the result with the sum. If the two are the same, the receiver assumes no error, accepts the five numbers, and discards the sum. Otherwise, there is an error somewhere and the data are not accepted.

## Slide 8: Example (Contd.)
We can make the job of the receiver easier if we send the negative (complement) of the sum, called the checksum. In this case, we send (7, 11, 12, 0, 6, −36). The receiver can add all the numbers received (including the checksum). If the result is 0, it assumes no error; otherwise, there is an error.

## Slide 9: Example - Complementary Checksum

## Slide 10: Complementary Checksum (Procedure)

## Slide 11: Complementary Checksum (Algorithm)
10.11

## Slide 12
10.12